## Slide 1: Operating Systems CS2006 Lecture: 2

## Slide 2: Computer-System Architecture

## Slide 3: What is a Computer System?

## Slide 4: Computer System
Consists of CPU and device controllers
Connected through a common Bus.
Providing access to shared memory
Each device controller is in charge of a specific device
  Disk drives
  Audio devices
  Video display

## Slide 5: Computer System Organization
Computer-system operation
  One or more CPUs, device controllers connect through common bus providing access to shared memory
  Concurrent execution of CPUs and devices competing for memory cycles

## Slide 6: Computer-System Operation
I/O devices and the CPU can execute concurrently
Each device controller is in charge of a particular device type
Each device controller has a local buffer
CPU moves data from/to main memory to/from local buffers
  Cf) DMA (Direct Memory Access)
I/O is from the device to local buffer of controller
Device controller informs CPU that it has finished its operation by causing an
interrupt

## Slide 7: Major Computer Components

## Slide 8: 1- CPU
Registers
  Program Counter (PC)
  Instruction Register (IR)
  Program Status Word (PSW)
  General-purpose registers
Instruction Set Architecture
  RISC vs. CISC
  Intel, SPARC, MIPS, PowerPC, ARM, Alpha, …
Pipelining
  Fetch, Decode, Execute, Write Back, etc.
Instruction-Level Parallelism(ILP)
  Superscalar vs. VLIW
  Simultaneous Multithreading

## Slide 9: Processor
Internal Register
  Memory Address Register (MAR)
    Specifies the address for next read or write
  Memory Buffer Register (MBR)
    Contains data written into memory or receives data read from memory
  I/O address register
  I/O buffer register

## Slide 10: User-Visible Register
May be read by user processes
Available to all programs – application programs and system programs
Types of registers
  Data
  Address
    Index
    Segment pointer
    Stack pointer
12

## Slide 11: Control and Status Register
Program Counter (PC)
  Contains the address of an instruction to be fetched
Instruction Register (IR)
  Contains the instruction most recently fetched
Program Status Word (PSW)
  Condition codes
  Interrupt enable/disable
  Supervisor/user mode

## Slide 12: 2- Memory Structure
Storage systems organized in hierarchy
  Speed
  Cost
  Volatility
Caching
  copying information into faster storage system
  main memory can be viewed as a last cache for secondary storage

## Slide 13: Storage-Device Hierarchy

## Slide 14: Memory Hierarchy

## Slide 15: Caching
Use of high-speed memory to hold recently-accessed data
Requires a cache management policy
  Write-through vs. Write-back
Caching introduces another level in storage hierarchy. This requires data that
is simultaneously stored in more than one level to be consistent
  Cache coherency

## Slide 16: Migration of A From Disk to Register

## Slide 17: 3- I/O Structure
After I/O starts, control returns to user program only upon I/O completion
  Wait instruction idles the CPU until the next interrupt
  Wait loop (contention for memory access)
  At most one I/O request is outstanding at a time, no simultaneous I/O processing
After I/O starts, control returns to user program without waiting for I/O
completion
  System call – request to the operating system to allow user to wait for I/O completion
  Device-status table contains entry for each I/O device indicating its type, address, and state
  Operating system indexes into I/O device table to determine device status and to modify table entry to include interrupt

## Slide 18: Device Controllers
I/O devices generally consists of two parts:
  An Electronic component: Device Controller
  A Mechanical component: The device itself
Each device controller is in charge of a specific device
It maintains
  Some local storage buffer
  A set of special purpose register
Accepts command from the Operating System
For example to read data from the device.

## Slide 19: Device Controllers
A Device controller might accept a command:
  Read
  Sector 11,206
The device controller would:
  Determine the current position of the head
  Move the head to the required location
  Accept data bit by bit
  Store in a local buffer
  Perform checksum on the data
Controllers contain small embedded programs to carry out all this work.

## Slide 20: Device Drivers
Who would initiate the controller
Who would determine read/write
Who would tell the sector number
A part of operating system called Device Driver
Software or Hardware?
  Software that talks to a controller
  Gives it command
  Accept Responses
Same for all controllers?
Different software for different type of controllers
Each controller manufacturer has to supply a driver for each operating system it supports

## Slide 21: Device Status Table
One entry per I/O device
Keeps record of
  Device’s type
  Address
  State
    Not functioning
    Idle
    Busy
If the device is busy, the new request is saved in a queue

## Slide 22: Device Status Table
9

## Slide 23: A Question
The operating system
  Gets an input
  Performs a computation
  Produces an output
  And Quits
  Yes or no?
The operating system is a Reactive Program

## Slide 24: Operating System
Modern Operating Systems are Interrupt driven
If
  No process to execute
  No I/O device to service
  No user to whom to respond
Then
OS will sit quietly, waiting for something to happen
This something is Interrupt
At a particular time either a user program is running or operating system is running

## Slide 25: Interrupts
 Interrupts are signals by external devices, normally I/O devices.They tell the CPU to stop its current activities and execute the appropriate part of the operating system.

## Slide 26: Types of Interrupts
There are three (or broadly two) types of interrupts:
  Hardware Interrupts
  Software Interrupts
  Traps

## Slide 27: Hardware Interrupts
 Hardware Interrupts - generated by hardware devices to signal that they need some attention from the OS.
 They may have just received some data (e.g., keystrokes on the keyboard or an data on the Ethernet card);
 or they have just completed a task which the operating system previously requested, such as transferring data between the hard drive and memory.

## Slide 28
Software Interrupts
 Software Interrupts are generated by programs when they want to request a system call to be performed by the operating system.

## Slide 29
Traps
 Traps are generated by the CPU itself to indicate that some error or condition occurred for which assistance from the operating system is needed.

## Slide 30: Interrupts and Traps
Interrupts are hardware interrupts, while traps are software- invoked interrupts.
The term Trap is used interchangeably with the term Exception (which is an automatically occurring software interrupt).

## Slide 31: Interrupts and Traps

## Slide 32: Simple Instruction Cycle
23

## Slide 33: Interrupts
Suspends the normal sequence of execution
Used to improve processor utilization

## Slide 34: Interrupt Handling
Different routines handle different type of interrupts.
Called Interrupt Service Routine (ISR)
When the CPU is interrupted it stops what it is doing
The address of the interrupted instruction is saved
A generic routine is run
  This routine examines the nature of interrupt
  Calls the corresponding ISR
The ISR’s are usually stored in the lower part of the memory
After the interrupt is serviced, the saved address is loaded to the Program Counter
The Interrupted computation can resume as though the interrupt had not occurred.

## Slide 35: Interrupt Cycle

## Slide 36: Interrupt Timeline
27

## Slide 37: Simple Interrupt Processing
28

## Slide 38
Multiple Interrupts
 Disable interrupts while an interrupt is being processed
29

## Slide 39
Multiple Interrupts
 Define Priorities for interrupts
30

## Slide 40: I/O Control
How does the kernel notice an I/O has finished?
  Polling
  Hardware interrupt

## Slide 41: I/O Control (Cont’d)
Device interrupts
CPU stops current operation, switches to kernel mode, and
saves current PC and other state on kernel stack
CPU fetches proper vector from vector table and branches to
that address (to routine to handle interrupt)
Interrupt routine examines device database and performs action required by interrupt
Handler completes operation, restores saved (interrupt state) and returns to user mode (or calls scheduler to switch to another program)

## Slide 42: I/O Interrupts
I/O requested by user program
Control transferred to OS
The Device Driver loads appropriate registers within the device controller
The device controller examines their contents
 If Read request:Transfer data from device to local buffer
Once the data transfer is complete informs the CPU by interrupt

## Slide 43: Two I/O methods

## Slide 44: 1. Synchronous I/O
The OS makes the CPU wait till the I/O complete interrupt is generated
How can a CPU wait, somehow it has to do F->D->E ??
Wait can be accomplished by jumping to an infinite loop code in OS:
Loop: jump Loop
If the devices does not support interrupts
They will just set a flag in their register to indicate I/O complete
The above loop would require to include Polling such devices as well

## Slide 45: 1. Synchronous I/O
If the CPU always has to wait for the I/O completion then the number of outstanding I/O requests is?
 Exactly One
So, whenever the I/O complete interrupt is generated the OS knows the source device
Drawback?
Excludes concurrent I/O operations to several devices

## Slide 46: 1. Synchronous I/O
35
Issues Read command to I/O module
Read status of I/O module
Read word from I/O module
Write word into memory
Check Status
Done
CPU -> I/O
I/O -> CPU
Error Condition
I/O -> CPU
CPU -> memory
Yes?
No
Ready
Not Ready
Next Instruction

## Slide 47: 2. Asynchronous I/O
Start the I/O request
Return control immediately to the user process
If the current user program cant run without the I/O, let the current process wait
CPU: Schedule some other user program or operating system code
  If no process ready to run, then still need the idle loop

## Slide 48: 2. Asynchronous I/O
The number of outstanding I/O requests is?
 More then One
Need to keep track of multiple I/O requests

## Slide 49: 2. Asynchronous I/O
Issues Read command to I/O module
Read status of I/O module
Read word from I/O module
Write word into memory
Check Status
Done
CPU -> I/O
Error Condition
I/O -> CPU
CPU -> memory
Ye?s
No
Ready
Next Instruction
Do something else
I/O -> CPU Interrupt

## Slide 50: 2. Asynchronous I/O
The I/O controller interrupts when it needs to be serviced
The OS determines the I/O controller
Processor reads the word of data from I/O controller to the memory
Updates the status in the Device Status table
In case of I/O complete interrupt, checks the additional request
The control is returned to the user program

## Slide 51: 3. Direct Memory Access (DMA)
Drawback of Asynchronous I/O?
Any data transfer must traverse a path through the processor
In case of DMA, the following info to the DMA module:
  Read or Write request
  Address of the I/O device
  Starting location in memory to read from or write to
  Number of words
The DMA module is then asked to start data transfer
The above operations are performed by Device Driver

## Slide 52: How a Modern Computer Works
A von Neumann architecture

## Slide 53: 3. Direct Memory Access
The processor can continue with its work
The DMA module transfer data directly from the device to the main memory
But how many accesses to memory are possible at a time
In order to do so, it has to “steal” cycles from processor…Cycle Stealing
Since, only one access to memory is possible at a time

## Slide 54: 3. Direct Memory Access
The processor has to wait in the mean while for memory
This would slow down the processor
But still more efficient than the previous two cases
After the block transfer is completed, a single I/O interrupt will be generated by the DMA module.

## Slide 55: 3. Direct Memory Access
Direct Memory Access
Issues Read command to I/O module
Read status of DMA module
Yes
Next Instruction
CPU -> DMA
Do something else
Interrupt DMA -> CPU

## Slide 56: Direct Memory Access (DMA)
Used for high-speed I/O devices able to transmit information at close to memory speeds
Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention
Only one interrupt is generated per block, rather than the one interrupt per byte
Bus arbitration between cache-memory and DMA transfers
Memory cache must be consistent with DMA
45

## Slide 57: Interrupts and Exceptions
Interrupts
  Generated by hardware devices
    Triggered by a signal in INTR or NMI pins (Pentium)
  Asynchronous
Exceptions
  Generated by software executing instructions
    INT instruction in IA32
    Page fault, protection fault
  Synchronous
  Trap (expected) or fault (unexpected)

## Slide 58: Reference
Chapter 1, Operating Systems by William Stallings
http://www.cs.toronto.edu/~demke/469F.06/Lectures/Lecture6.pdf
http://www.tldp.org/LDP/tlk/dd/interrupts.html
http://en.wikibooks.org/wiki/Operating_System_Design/Processes/Interrupt
http://www.slideshare.net/guest2e9811e/interrupts
https://amser.org/g11619
http://www.eecs.harvard.edu/~mdw/course/cs161/notes/osstructure.pdf
http://www.sci.brooklyn.cuny.edu/~jniu/teaching/csc33200/files/0910- ComputerSystemOverview02.pdf
http://siber.cankaya.edu.tr/OperatingSystems/ceng328/node87.html
http://www.personal.kent.edu/~rmuhamma/OpSystems/Myos/processControl.htm
http://www.tutorialspoint.com/operating_system/os_processes.htm
http://wiki.answers.com/Q/Explain_process_control_block
https://msdn.microsoft.com/en-us/library/windows/desktop/aa365683(v=vs.85).aspx